OV7670

Modes

Reference

OV7670 Camera General Subsystems

These notes are a disjointed set of observation on the setup for the OV7670. They might be useful to somebody that is not familiar with reading a data sheet, sorry for the poor organization.

The OV7670 has a large number of adjustments that are used to produce the best possible picture. Each of these adjustments are (largely) independent of the format of the camera output. An example is the “Edge” adjustment, it is valid in the VGA,QVGA,CIF and QCIF mode. It is then reasonable to treat these adjustments as separate, but common, functions to be applied equally to all the photos taken by the camera. This is (I hope) an exhaustive list of the functions.

Within the mode writeup all the relevant registers are named. The value of the register on a reset is shown in its first appearance as “0x## REG = 0x## = #### ####” the location of the register is in HEX, the register name is that given in the documentation, the value in HEX after the first “=” is the reset value. If the register has bits to be set to enable/disable functions the second “=” precedes the value in binary separated into two four bit nibbles, to allow easy reference to the reset modes set. Specific bits in a register are called out by [#] for a single bit or [#:#] for a collection of two or more bits. Dividing the document sections to address a specific function will require that some bits in a register that has two (or more) functions not be addressed in all sections.

# Analog/Digital Control
This register group is not documented well. Could find no change in picture by changing values of ADCCFTR0.
0x20 ADCCTR0 = 0x04 = 0000 0100 - “ADC Control”
[3] ADC range adjustment. 0 = 1 x Range, 1 = 1.5 x Range
0x20 ADCCTR0[2:0] ADC reference adjustment. 000 = 0.8 x, 100 = 1 x, 111 = 1.2 x
0x21 – 0x23 ADCCTR1 to ADCCTR3 are “reserved”

# Automatic Exposure Control AEC
Very important function. The details are in the Implementation Guide. There are two different modes defined. The Histogram based and the Average based. The important thing to know is that the AEC and the Automatic Gain Control are interrelated and that the AEC will be adjusted before the AGC which acts to adjust and center the AEC. They both share the same registers. There is disagreement between the spec sheet and the Implementation Guide about the role of COM4. The actual action of these two modes are not consistent, some resolutions won't respond to the “AEC Average”. QVGA and QCIF have black screen when in AEC Average but work when in the AEC Histogram mode, but don't switch out of the “black screen” mode until a “Reset” is given. This may be a program bug, if so I can't find it.
Insert command here?
The Implementation Guide defines COM4 as “Average Luminance Calculation Window” and then proceeds to define bits [5:4] as:
- 00 = Full frame
- 01 = Center half frame
- 1x = Center quarter frame.
The data sheet for the OV7670 defines COM4 as “Common Control 4” where bits [5:4] are defined as:
- 00 = Full window
- 01 = ½ window
- 10 = ¼ window
- 11 = ¼ window
with the caution that COM17[7:6] “AEC window” must match the setting of COM4[5:4].
The description of the method by which the AEC is done is a combination of fast search followed by a slow (smaller step size) search within the “Stable Operating Region”. The following quote is taken from the Implementation Guide of 2 September 2005. A partial URL is: web.mit.edu/6.111/www/f2015/.../OV7670app.pd This is the result of a Google search “OV7670 +"Implementation Guide" it is the second entry on the page. The first is the same document but I didn't figure out how to download it.
“As shown in Figure 3-1, the average-based AEC/AGC algorithm changes the luminance average value step by step until it converges with Stable Operating Region. Outside the Control Zone, the AEC/AGC adjusts exposure time and gain in large steps to change the luminance level fast. Once inside the Control Zone but still outside the Stable Operating range, the AEC/AGC adjusts exposure time and gain in smaller steps to make the luminance level converge with the Stable Operating Region smoothly. When finally inside the Stable Operating Region, the AEC/AGC no longer adjusts the exposure time and gain.”
Given all of this it looks like the “Stable Operating Region” is the part that is most critical to taking a good picture. For starters setting the bits that control the AEC operation requires that registers:
- 0x13 COM8[7] 0 = Normal speed, 1 = enable fast AGC/AEC algorithm
- 0x13 COM8[0] 1 = AEC enable
- 0xAA HAECC7[7] 0 = Average based AEC, 1 = Histogram based AEC
- 0x42 COM17[7:6] and 0x0D COM4[5:4] both have to be set to the AEC window size desired

Then the values for the “Stable Operating Region” are set along with the “fast mode zone” control nibbles to allow rapid convergence to the desired region. All this is just for the Average based AEC. The histogram based AEC is another problem.

Registers on Reset
0x13 COM8 = 0x8F = 10000 1111	Common Control 8
0x13 COM8[7] 0 = Normal speed, 1 = enable fast AGC/AEC algorithm
0x13 COM8[6] AEC step size control 0 = limited to Vertical blanking, 1 = Unlimited step size
0x13 COM8[0] 1 = AEC enable
0x14 COM9 = 0x4A = 0100 1010	Common Control 9
COM9[0] 1 = Freeze AGC/AEC
0xAA HAECC7[7] aka NALG[7] = 0x14 = 0001 0100 Note: HAECC7 is in the data sheet, NALG is	in the application note and defined as “AEC Algorithm selection” .

HAECC7[7] 0 = Average based AEC, 1 = Histogram based AEC
HAECC7[6:0] = Reserved

0x24 AEW[7:0] = 0x75 – AGC/AEC Stable Operating Region (Upper Limit)
0x25 AEB[7:0] = 0x63 – AGC/AEC Stable Operating Region (Lower Limit)
0x26 VPT = 0xD4 = 1101 0100 AGC/AEC Fast Mode Operating Region
[7:4] – High Nibble of upper limit of fast mode zone control, default 0xD
[3:0] – High Nibble of lower limit of fast mode zone control, default 0x4
0x42 COM17 = 0	Common Control 17
bits[7:6] AEC window ( must be same as COM4[5:4]) 0=Normal,1 = ½, 2 = ¼, 3 = ¼
0x0D COM4 = 0	Common Control 4
COM4[5:4] (must be same as COM17[7:6] 0=Full Window,1 = ½, 2 = ¼, 3 = ¼
Again notice the difference in the definitions of “Normal” and “Full Window” in the spec sheet.
Here is the definition from the Implementation Guide!
0x0D COM4 Average Luminance Calculation Window
COM4[5:4] 00 = Full Frame, 01 = Center half frame and 1x Center Quarter frame

## Histogram Based AEC/AGC Control
This method is complex enough that if you attempt it you should use the Implementation Guide. It involves the probabilities of the luminance to control the AEC. The explanation leaves something to be desired (mainly it was written by an engineer that knows too much about it to explain it to a programmer). Matters are made more confusing by the renaming of the registers between the documentation, read the Implementation Guide! I did find that the picture was a little brighter if I changed the values of HAECC1 to oxB0.
Registers on Reset per the OV7670 Data Sheet
0x9F HAECC1 = 0xC0	Histogram Based AEC/AGC Control 1
0xA0 HAECC2 = 0x68	Histogram Based AEC/AGC Control 2
0xA6 HAECC3 = 0xF0	Histogram based AEC/AGC control 3 - 6
0xA7 HAECC4 = 0xC1
0xA8 HAECC5 = 0xF0
0xA9 HAECC6 = 0xC1

Registers on Reset per the Implementation Guide

0x9F HRL = 0xC0	High Reference Luminance
0xA0 LRL = 0x90	Low Reference Luminance
0xA6 LPH = 0xF0	Lower Limit of Probability for HRL, after exposure/gain stabilizes
0xA7 UPL = 0xC1	Upper Limit of Probability for LRL, after exposure/gain stabilizes
0xA8 TPL = 0xF0	Probability Threshold for LRL to control AEC/AGC speed
0xA9 TPH = 0xC1	Probability Threshold for HRL to control AEC/AGC speed

# Automatic Gain Control AGC
The Automatic Gain Control interacts with the Automatic Exposure Control. According to the “Implementation Guide” the AEC takes president over the AGC. It can be setup independently of the AGC. The values of the registers COM8[2], COM9[6:4] and the two registers that hold the gain value (VREG[7:6] and GAIC[7:0] make up a ten digit binary number). These registers are “read only” if the AGC is enabled, and may be set to any value when that AGC is disabled. The AGC can make a great difference in the picture quality.
Define commands here?
The “Fast AGC/AEC Select” COM8[7] is set by default to enable this function
The “Freeze AGC/AEC” bit COM9[0] is cleared by default
Registers on Reset
0x13 COM8 = 0x8f = 1000 1111
COM8[7] Fast AGC/AEC Select
COM8[2] AGC Enable Select
0x14 COM9 = 0x4a = 0100 1010
COM9[6:4] Automatic Gain Ceiling – Maximum AGC value ( 8 )
COM9[3:1] Reserved
COM9[0] Freeze AGC/AEC turned off
0x00 GAIN = 0x04 = 0000 0100	Gain register – both R/W and RO depends on AGC on/off
GAIN[7:0] – eight bits of a 10 bit gain value (LS 8 bits)
0x03 VREF = 0 Vertical Frame Control
VREF[7:6] = bits [9:8] of 10 bit gain value (MS 2 bits)
# Automatic White Balance
There are actually three modes of White Balance
- Manual Mode – R,G,& B are set manually.
- Normal – the DSP makes the R,G & B average values equal.
- Advanced – the DSP adjusts R,G & B based on color temperature.
This seems so critical that there should be some information on what the registers AWBCTRx actually contain. The implementation guide goes into detail about the bits of AWBCTR0. The implementation guide also names AWBC1 to AWBC12 (0x43-0x48 & 0x59 to 0x5E) as used but they depend on the lens, so contact OmniVision FAE for these settings. Turns out that the FAE is a Linkedin page. It is interesting to note that the camera comes up in the Advanced mode on reset.
See section 5.1.2 of the implementation guide for manual control of the AWB.
0x13 COM8 = 0x8F = 1000 1111
COM8[1] 0 = Disable (manual), 1 = Enable (automatic mode)
0x41 COM16 = 0x08	= 0000 1000	Common Control 16
bit[3] = 1 AWB Gain Enable set.
Bit[1] 1 = Color Matrix coefficient double option set.
0x6F AWBCTR0 = 0x9A = 1001 1010
AWBCTR0[0] 0 = Advanced Mode, 1 = Normal Mode
AWBCTR0[3] 0 = Adjust Red and Green gain only, 1 = Adjust Red,Green and Blue gain
AWBCTR0[2] 0 = Maximum Gain x2, 1 = Maximum Gain x4
0x6E AWBCTR1 = 0xC0
0x6D AWBCTR2 = 0x55	Registers 0,1,2 and 3 preset by a reset command
0x6C AWBCTR3 = 0x02	Average White Balance Control Registers
0x01 BLUE[7:0]	Blue channel gain
0x02 RED[7:0]	Red channel gain
0x6A GGAIN[6:0]	Both Gr and Gb
0x5F B_LMT = 0xF0 = 1111 0000	AWB B Gain Range Note: Defined in Implementation, Data Sheet
has it marked as RSVD
B_LMT[7:4] = 0xF No operational definition
B_LMT[3:0] = 0x0 No operational definition

0x60 R_LMT = 0xF0 = 1111 0000 AWB R Gain Range – as above no data defined.

0x61 G_LMT = 0xF0 = 1111 0000 AWB G Gain Range – as above no data defined.

0x69 GFIX = 0x52 = 0101 0010 AWB Pre-Gain
GFIX[7:6] = 00 = 1x, 01= 1.25x, 10 = 1.5x and 11 = 1.75x Gr channel pre gain
GFIX[5:4] = 00 = 1x, 01= 1.25x, 10 = 1.5x and 11 = 1.75x Gb channel pre gain
GFIX[3:2] = 00 = 1x, 01= 1.25x, 10 = 1.5x and 11 = 1.75x Red channel pre gain
GFIX[0:1] = 00 = 1x, 01= 1.25x, 10 = 1.5x and 11 = 1.75x Blue channel pre gain

# Black Level Adjustment
The Black Level Calibration cannot be turned off, see ABLC[2] definition. The Automatic Black Level calibration when turned on will adjust the black level compensation for each channel AD_CHXx. The lower black level limit THL_ST and the stable range of black level THL_DLT are set by the reset command. If the Automatic Black Level Calibration is turned off ABLC[2] = 0 then any adjustment must be done manually.
The software turns on this bit for all modes.
0xB1 ABLC1 = 0
ABLC1[2] 0 = Disable Enable Automatic Black Level Calibration – Black Level Calibration is	still active. Set 1 to enable Automatic Black Level Calibration
0xB3 THL_ST = 0x80	Lower Limit Black Level + 0x80
0xB5 THL_DLT = 0x04	Stable Range of Black Level
0xBE AD-CHB[6:0] = 0	Blue channel black level compensation
0xBF AD-CHR[6:0] = 0	Red channel black level compensation
0xC0 AD-CHGb[6:0] = 0	Gb channel black level compensation
0xC1 AD-ChgR[6:0] = 0	Gr channel black level compensation

# Brightness
The brightness command is used to lighten or darken the picture. A single register is used.
The software implements this as a command “bright=[2,1,0,-1,-2]”.
0x55 BRIGHT = 0	BRIGHT Brightness Control
[7] Sign 0 = Positive, 1 = Negative
values of 0x00 and 0x80 mean no adjustment. Register values of 0 and 0x80 can be interpreted as + and – zero.
Documentation recommends levels +2,+1,0,-1,-2 with the corresponding hex values of
0x30,0x18,0x00,0x98,0xb0. Note the sign bit of the last two.

# Color Channel Bias

The bias registers are controlled by a bit that is in a common control register (0x0F COM6) and the bit is “reserved”. Setting gamma COM13[7] and doubling the color matrix COM16[1] are two settings that are useful. UV Average REG4B[0] enable may be good to have but I won't know will I write some software, UV Automatic Adjustment COM13[6] looks like another candidate for tests, but need to explore values for 0xC9 SATCTL first.
Matrix double bit has some effect on output – makes it darker.
Changing 0x3D COM13[6] – causes the size of the pic and the color both to change ?
This is with 0x4B REG4B[0] = 1 UV Average enabled. Appears to change the uyvy to vyuy? It also changes the scan for CIF,QCIF.
0x0F COM6 = 0x43 = 0100 0011	Common Control 6

This register is defined as used to control bias adjustments, BUT the bit is reserved.
0x3D COM13 = 0x88 = 1000 1000	Common Control 13
bit[7] Gamma Enable
bit[6] UV Automatic Adjustment this sets 0xC9 SATCTL[3:0], SATCTL[7:4] has
minimum == 1100.

0x41 COM16 = 0x80 = 1000 0000	Common Control 16
bit[1] Color Matrix coefficient double option

0x4B REG4B = 0	Register 4B – UV Average enable
bit[0] Enable UV Average

0x27 BBIAS = 0x80	B Channel signal Out Bias (effective only when 0x0F COM6[3] = 1) however the spec sheet defines COM6[3] as “reserved”
0x27 BBIAS[7] 0 = Add Bias, 1 = Subtract Bias
0x27 BBIAS[6:0] Bias Value of 10 bit range
0x28 GbBIAS = 0x80	Gb Channel signal Out Bias (effective only when 0x0F COM6[3] = 1) however the spec sheet defines COM6[3] as “reserved”
0x28 GbBIAS[7] 0 = Add Bias, 1 = Subtract Bias
0x28 GbBIAS[6:0] Bias Value of 10 bit range
0x2C RBIAS = 0x80 R Channel signal Output Bias (effective only when 0x0F COM6[3] = 1) however the spec sheet defines COM6[3] as “reserved”
structure as above.
0xBE AD-CHB = 0x00	Blue Channel Black Level Compensation
0xBF AD-CHR = 0x00	Red Channel Black Level Compensation
0xC0 AD-CHGb = 0x00	Gb Channel Black Level Compensation
0xC1 AD-CHGr = 0x00	Gr Channel Black Level Compensation

0xC9 SATCTR = 0xC0	Saturation Control
bits[7:4] UV saturation min
bits[3:0] UV saturation result

# Color Correction
The notes specify several values for this matrix. It is defined as 2,1,0,-1,-2 but the values are specified in the document. It is implemented in the software as saturation=[2,1,0,-1,-2] also the command saturation? will report the current value.
0x41 COM16 0x08 = 0000 1000	Common Control 16
bit[1] Color Matrix coefficient double option

0x4F MTX1 = 0x40	YUB Color Matrix registers MTX1 to MTX6
0x50 MTX2 = 0x34
0x51 MTX3 = 0x0C
0x52 MTX4 = 0x17
0x53 MTX5 = 0x29
0x54 MTX6 = 0x40

0x58 MTXS = 0x1E	Matrix Coefficient Sign for MTX1-6
bit[7] Auto Contrast Center enable
bits[5:0] Matrix coefficient sign bits

The OV7670 software Application Note recommend several different sets of values in the range of +2 to -2 in steps of one. Values are given in the Application Note. See pages 14 & 15. However none of the values match the reset default values. Design change or manufacturing calibration what?

0x69 GFIX = 0	Fixed Gain Control
bits[7:6] Gain for Gr Channel, bits[5:4] Gain for Gb Channel, bits[3:2] Gain for R Channel,
bits[1:0] Gain for B Channel
All channels have the same encoding: 0 = 1, 2 = 1.5, 3 = 1.75

# Contrast
Two registers hold values that control the respective elements of the picture. The proviso is that the CONTRAS_CENTER is either set by the hardware (0x58 MTXS[7] = 1) or set manually if the bit is zero. CONTRAS_CENTER is not defined anywhere and defaults to 0x80.
The software has a contrast command contrast=[2,1,0,-1,-2]. This command sets CONTRAS to various values specified in the application notes. It takes effect on the next picture capture, but may take time to stabilize to the final value. This is a common problem with the camera. The contrast register can be set even when the contrast control is in automatic.
0x56 CONTRAS = 0x40	CONTRAS Contrast Control
0x57 CONTRAS_CENTER = 0x80	Contrast Center Control
0x58 MTXS = 0x9E = 1001 1110
MTXS[7] = 1 to use hardware control.

# Edge Enhancement
The hardware can “sharpen” the image by enhancement of the edges. This results in greater contrast. The control over this if COM16[5]. If this bit is set then the edge enhancement is active and the register EDGE will be filled with a value. If the bit is not set then the value in EDGE will still be used! This is one more place in the camera where there is a dual mode register. EDGE is R/W if the enhancement is off and if enhancement is on EDGE is a R only register. On reset the content of the register is set to zero.
A command edgevalue=[0-32] is implemented. The current value may be checked using the command edge? which will return the value of the edge register.
Registers on reset
0x41 COM16 = 8	Common Control 16
bit[5] Enable edge enhancement threshold auto-adjustment for YUV.
See EDGE[4:0] to set the edge value.

0x3F EDGE = 0	Edge Enhancement Factor
bit[4:0] can be set by software.

Range is controlled by registers REG75[4:0] and REG76[4:0]

0xc75 REG75 = 0x0F = 0000 1111	Edge Enhancement Value Lower
bits [4:0] Edge Enhancement Lower Limit
0x76 REG76 = 0x01 = 0000 0001	Edge Enhancement Value Upper
bits[4:0] Edge enhancement upper limit

# Denoise Modes
The denoise function operates in two modes, Manual and Automatic. The default is manual (0x41 COM16[4] = 0) and the controlling register is 0x4C DNSTH[7:0]. The denoise threshold is set by this register, the default is 0. The Automatic mode (0x41 COM16[4] = 1) has the offset set by 0x77 REG77[7:0], the default for this register is 0x10.
There are five commands in the software for this mode.
Denoise? - display the denoise registers.
Denoiseon – turn on denoise
denoiseoff – return denoise to automatic mode
denoisethreshold=[ 0 – ff] – set denoise offset
denoisisereg77=[0-ff] – set denoise offset in automatic mode, default is 0x10.
Registers at reset
0x41 COM16 = 08
COM16[4] 0 = Manual, 1 = Automatic
0x4C DNSTH = 0
DNSTH[7:0] in Manual set to a threshold value, in Automatic receives adjusted value.
0x77 REG77 = 0x10 = 0001 0000
REG77[7:0] Default is 0x10, can be set to any value 0 - 25410
# Exposure Control
Manual exposure control is not enabled by default (0x13 COM8[0] = 0), auto-adjustment is set by the reset command 0x13 COM8 = 0x8F = 1000 1111. This turns on several mode items including the automatic exposure control AEC, the automatic gain control AGC, automatic white balance AWB and the “fast” AGC/AEC algorithm. Set 0x13 COM8[0] = 0 to use the manual exposure.
Manual exposure control, actually the “exposure time” can be manually controlled by using the registers defined below. The calculation of the time is Exposure time = AEC[15:0] * trow_interval. The value of trow_interval = 2 * ( 784 + DUMMY_PIXELS) * tint_clk. DUMMY_PIXELS are the count in the two registers 0x2A EXHGC[7:4] MS 4 bits and 0x2B EXHCL[7:0], both of these registers are set to zero on a “reset” command. The “Automatic Exposure Control” AEC [15:0] is contained in the following registers.
Register at reset
0x13 COM8 = 0x8F = 1000 1111
0x13 COM8[0] 0 = AEC off, 1 = AEC on.
0X07 AECHH[5:0] = 0x40 = 0100 0000
0x10 AECH[7:0] = 0x7F = 0111 1111
This appears to be a misprint in the data sheet. The sum of the bits defined is 14 not 15. This manual control would appear to have little utility except in circumstances where the light could be controlled by the user of the camera.

# Exposure Modes

There are two modes – Night Mode and normal. The night mode modifies the exposure and the frame rate. Setting 0X3B COM11[7] = 1 will enable the night mode. COM11[6:5] sets the minimum frame rates.
Register at reset
0x3B COM11 = 0
0x3B COM11[7] 1 = Night Mode
0x3B COM11[6:5] Frame rate selection bits, night mode.
1. 00 – normal frame rate.
2. 01 = ½ normal frame rate.
3. 10 = ¼ normal frame rate.
4. 11 = 1/8 normal frame rate.

# Format Selection
Format selection is done by specifying the type of photo to be taken and defined as:
VGA	- raw Bayer output
VGAP – processed Bayer output
VGAW – Windowed VGA, select window using window=x,y,x,y command.
QVGA – Quarter VGA
CIF – some format
QCIF – Quarter CIF
QQVGA – a 40 x 30 format
Q8060 - an 80 x 60 format
0x12 COM7 = 0
0x12 COM7[7] = 1, Reset all registers to their default values and select VGA format.
0x12 COM7[5:3] one bit set in this group selects a format for the picture
COM7[5:3] decode as follows:
bit 5 – CIF Selected
bit 4 – QVGA Selected
bit 3 – QCIF Selected
All bits off – VGA selected
The HSTART/HSTOP & VSTART/VSTOP get setup correctly at the time that the bit is changed. The SCALE and DWC bits (COM3[3:2]) are not changed.
Formats not in the selection list are derived from the use of several register that specify division of the DSP clock and the dividers that control the formating of the data on a line by line basis. This will be discussed later in this document.

# Frame Rates
Frame rates are a function of the input clock ( usually a crystal) the PLL multiplier and the clock divider. There are tables in the OV7670 Software Application Note. The registers that are used are shown in the bullet list with reset default values.
- 0X11 CLKCR 0x80 – Internal Clock: Select and prescale. The reserve bit is set only.
- 0X6B DBLV 0x0A – PLL control. The reserve bits are set, the divider[7:6] is bypass PLL.
- 0X2A EXHCH 0x00 – Dummy Pixel Insert MSB
- 0X2B EXHCL 0x00 - Dummy Pixel Insert LSB
- 0X92 DM_LNL 0x00 – Dummy Line low 8 bits
- 0X93 DM_LNH 0x00 – Dummy Line high 8 bits
The camera I have has a 12Mhz crystal. I use the PLL x4 and the divider value 2 to get a 24Mhz PCLK (this code is in the reset command).
# Lens Correction
This one is part of the “contact the factory” adjustments.
0x94 LCC6 = 0x50	Lens Correction Option 6
0x95 LCC7 = 0x50	Lens Correction Option 7

# Light Banding
Banding is when a light generated by florescent light is used to illuminate the scene. The light flicker is faster than the exposure time and results in areas (bands) of over and under exposure.
The software implements the following commands:
- banding? - display the banding settings
- banding=[50hz,60hz,auto,off]

There are two modes - “Auto-detect” and “manual”. Auto-detect is set by COM11[4] =1, the manual mode requires setting two bits (COM8[5] turn on filter) and (COM11[4] select 50Hz or 60Hz filter).
Registers are reset
0x13 COM8 = 0x8F = 1000 1111
COM8[5] Band Filter ON/OFF see BD50ST & BD60ST
0x3B COM11 = 0
COM11[4] Band Filter Frequency auto detect ON/OFF
COM11[3] select BD50ST or BD60ST banding filter values
0x9D BD50ST = 0x99	50 Hertz Banding Filter Value
(only when COM8[5] and COM11[3] are high)
0x9E BD60ST = 0x7F	60 Hertz Banding Filter Value
(only when COM8[5] = 1 and COM11[3] = 0)

0xA5 BD50MAX = 0x0F	50 Hertz Banking step limit
0xAB BD60MAX = 0x0F	60 Hertz Banding Step Limit

# Data Output Format
On reset data output format is set for UYVY output.
The software implements the output options:
- output? - Display the current output mode.
- yuyv - one of the YUV options.
- yvyu – another one of the YUV options.
- uyvy – the most common YUV option.
- rgb565 – a converted YUV option.
- Rgb555 – a less common option.
- Rgb444x – a four bit version with the last nibble zeros.
- Rgbx444 – a four bit versioj with the first nibble zeros.
- Bayerraw – read manual to find out about this.
- Bayerprocessed – same as above
      The command is output=[ one of the above] to set an option, to check the option use 'output?'
The following register are set as shown.
0x12 COM7 = 0
0x3A TSLB = 0x0D = 0000 1101
0x3D COM13 = 0x88 = 1000 1000

0x40 COM15 = 0xC0 = 1100 0000

0x8C RGB444 = 0

Output formats are YUV, RGB and Bayer. The variations on these basic outputs are selected by modification of bits in these registers.
COM7 / [2]	COM7 / [0]	TSLB / [3]	COM13 / [0]	COM15 / [5]	COM15 / [4]	RGB444 / [1]	RGB444 / [0]	Output Format
0	0	0	0	0	0	0	0	YUYV
0	0	0	1	0	0	0	0	YVYU
0	0	1	0	0	0	0	0	UYVY
0	0	1	1	0	0	0	0	VYUY
1	0	0	0	0	1	0	0	RGB565
1	0	0	0	1	1	0	0	RGB555
1	0	0	0	0	0	1	0	RGBx444
1	0	0	0	0	0	1	1	RGB444x
0	1	0	0	0	0	0	0	Bayer Raw
1	1	0	0	0	0	0	0	Processed Bayer Raw

There is a bug in the documentation. Explore to fix COM13[0] The writeup for TSLB says COM13[1] is used is selection of the various YUV modes, so does COM13[1] except it shows bit zero instead. COM13[5:1] are reserved. Checks show that its COm13[0]. When switching between various resolutions the output will change, don't know why. For example in QVGA with output set to UYVY, if you switch to CIF without changing the output, the data output will be VYUY so the colors are wrong. Why the output format is switched by changing the resolution is not documented. This problem is compounded when using the RGB565 format. It appears that it simply does not work although it could be a bug in my code or the modifications I made to the LCD library. The LCD library looks OK because a good RGB565 picture from an outside source is rendered correctly.
0x12 COM7 = 0
0x12 COM7[2] = select RGB (with other bits) see bit[0]
COM7[2]	COM7[0]
     0	0	YUV format output (TSLB & COM13)
        1	0	RGB format output (COM15 & RGB444)
     0	1	Bayer RAW	1	1	Processed Bayer RAW
0x3A TSLB = 0x0D = 000 1101
0x3A TSLB	Line Buffer Test Options
bit[4] use fixed UV values (MANU & MANY),
bit[3] YUV control, see data sheet and 0x3D COM13[1] or COM[0], typo in spec sheet?

0x3D COM13	Common Control 13
 bit[0] UV Swap bit (see TSBL[3]) – YUYV, YVYU,UYVY,VYUY
TSLB[3]	COM13[1]
    0	0	YUYV
    0	1	YVYU
    1	0	UYVY
    1	1	VYUY

0x40 COM15 = 0	Common Control 15
COM15[7:6] Output format range select – 0-FF,1-FF,10-FF.
COM15[5:4] RGB555/565 option – see data sheet also COM7[2] and COM7[0] and RGB444[1]
Bit 5	Bit 4
  x	0	Normal RGB output
  0	1	RGB565 only when RGB444[1] is 0
  1	1	RGB555 only when RGB444[1] is 0

0x8C RGB444 = 0	RGB Word Format Filler select
RGB444[1] RGB444 enable ( see COM15[4])
RGB444[0] RGB444 word format 0 = xRGB, 1 = RGBx

# Picture Correction
After reset the picture correction is setup for the following items/conditions
- Manual De-noise, strength set to zero.
- Digital Gain controlled by VREF[7:6], VREF[7:6] = 0.
- Black/White Pixel Correction turned off.
0x41 COM16 = 0X08 = 000 1000
COM16[4] 0 = Manual Mode, denoise strength set by DNSTH
    1 = Automatic mode strength is adjusted and saved in DNSTH
0x4C DNSTH = 0	De-noise Strength, both input and output
0x77 REG77[7:0] = 0x10	De-noise Offset ( only in automatic mode)

0x74 REG74 = 0	Digital Gain Control
REG74[4] 0 = Gain Control by VREF[7:6]
REG74[4] 1 = Digital Gain Control by REG74[1:0]
REG74[1:0]
[1]	[0]	Digital Gain
 0	0	Bypass
 0	1	1x
 1	0	2x
 1	0	4x

0x76 REG76 = 0x01 = 0000 0001	Register 76
REG76[7] Black pixel correction enable
REG76[6] White pixel correction enable

# Scaling
This function is used both by the defined formats and the special formats that are programmed.
Two registers control the scaling: SCALING_XSC and SCALING_YSC. They implement a fractional ratio that is inverse of what you would expect, the ratio is smaller than one but the result is the inverse and the picture grows larger. Only in the sense of a zoom function within the format already selected.
Both registers are defined as being used and the numerator of the hex fraction value is 0x20. The default for the two registers are 0x70 SCALING_XSC = 0x3A (5810) and 0x71 = 0x35 (5310). The dividend is 3210 so the X scaling ratio is 0.55 and the Y scaling ratio is 0.60. The register 0x0C COM3 has two bits that control if scaling and “down sampling” are enable. Control bit 0X0C COM3[3] if set to a one allows the scaling to be enabled. Control bit 0x0C COM3[2] set to a one enables the “down sampling”. The bit that controls if the ratio can be adjusted by the user is in 0x3E COM14[3] - “ scaling parameter can be adjusted manually” and more importantly 0x3E COM14[4] bit controls if both DCW and SCALING can be used, see COM3 also. If COM14[4] is a zero (default) then the “normal PCLK” is used if a one then both 0x3E COM14[2:0] and 0x73 SCALING_PCLK_DIV[3:0] are used. It turns out that COM14[2:0] is relatively easy – it just divides the clock by a fixed amount (1,2,4,8 and 16). The real work gets done by 0x73 SCALING_PCLK_DIV which controls the pixel clock. That determines the number of pixels on a line. The use of these two registers and the X and Y scaling registers allow many different formats to be generated. All the special formats in the software simply set the divisor ratio to one by storing a 0x20 in the registers. Getting the scaling to work needs to be worked on I can get it to work sometimes but not others.

## Down Sampling a Format
This is the way all of the predefined output are obtained. The basic output is the VGA format with a size of 640 x 480 pixels.
Enabling the DWC and SCALING by setting COM3 bits and the adjusting the clock via COM14[2:0] performs the basic scaling function. The pixel clock must be adjusted by setting bits in the 0x73 SCALING_PCLK_DIV[2:0] bit positions. A portion of code will show the method used for manual formats. This code sets a 40 x 30 size picture format.
 setReg(COM3,BIT3 |BIT2); // enable scaling [3] and down sampling [2] clearReg(COM14,0x1F); // clear bits [4:0] - DCW[4] & Scaling ctl[3] PCLK divider[2:0] setReg(COM14,0x1C); // DCW enable, Scaling enable and PCLK divider set to 16 setReg(SCALING_DCWCTR,0x33); // set down sampling to divide by 8 OV7670WriteReg(SCALING_XSC,0X40); // set to a scaling factor of X1/2 for now OV7670WriteReg(SCALING_YSC,0X40); OV7670WriteReg(SCALING_PCLK_DIV,0X0A); // [3] = divide enable, [2:0] = divide by 4
The rest of the code to setup the format is to set the “window” registers to predefined values and then call the routine “generalSetup();” which set the bits in the control registers for the format and other items that are not determined by the reset which always precedes a change in format.

Registers on reset
0x0c COM3 = 0
0x0c COM3[2] = 0	DCW enable if set to 1.
0x0c COM3[3] = 0	SCALING enable if set to 1.
0x3E COM14 = 0
0x3E COM14[4] = 0 DCW and PCLK enable -see SCALING_PCLK_DIV and COM14[2:0]
0x3E COM14[3] = 0 Manual scaling enable. Predefined formats (CIF,QCIF,QVGA) can be adjusted manually.
0x3E COM14[2:0] = 0 PCLK divider 0 -1 (binary) divide by 1,2,4,8 and 16
0x73 SCALING_PCLK_DIV = 0
[3] = Bypass clock divider for DSP scale control.
[2:0] 0 – 4 Binary = 1,2,4,6,16 divide ratio.
0x3E COM14 = 0	Common Control 14
COM14[4] = 0 is Normal PLK
COM14[4] 1 = DCW and PCLK controlled by 0X3E COM14[2:0] and
0X73 SCALING_PCLK-DIV[3:0]
COM14[3] 0 = Scaling parameters cannot be adjusted manually.
COM14[3] 1 = Scaling parameters can be adjusted manually.
COM14[2:0] values 0 through 4 = 1,2,4,8,16 divide

0x70 SCALING_XSC = 0x3A	Test Pattern Control and Horizontal Scaling Register
bit[7] Test Pattern Selection (see also SCALING_YSC[7]
bits[6:0] Horizontal Scale Factor – see app. note 2 Sept. 2005

0x71 SCALING_YSC = 0x35	Test Pattern Control and Vertical Scaling Register
bit[7] Test Pattern Selection (see also SCALING_XSC)
bits[6:0] Vertical scale factor – see app. Note 2 Sept. 2005

0x72 SCALING_DCWCTR = 11	DCW Control ( guess “down count window”)
bit[7] Vertical Average calculation
bit[6] Vertical down sampling
bits[5:4] Vertical down sample rate
bit[3] Horizontal average Calculation option
bits[1:0] Horizontal down sample rate

0x73 SCALING-PCLK_DIV = 0x00	Scaling PCLK Divider
bit[3] Bypass clock divider for DSP scale control
bits[2:0] Divide ratio 0=1,1=2,2=4,3=8,4=16

0xA2 SCALING_PCLK_DELAY: T 2 R 2	Pixel Clock Delay
bits[6:0] Scaling output delay

0xA4 NT_CTRL	Frame Timing Control
bit[3] Auto frame rate adjustment 1= Reduce frame rate by half
bit[1:0] Auto frame rate switch point – 0 = insert dummy at 2x gain, 1 = insert dummy row at 4x	gain, 2 = insert dummy row at 8x gain

# Special Effects
After a reset all special effects and the “Strobe” options are turned off. Strobe is brought out on the pins of some of the camera chips. Could be used for flash or for testing.
The software implements some of these functions:
antique - brownish picture
bluish
greenish
redish
bw - hardware generated black and white image
colornegative
bwnegative - hardware generated black and white negative
normal - default
Flip vertical – flipyes/flipno
mirroryes
mirrorno

0x1E MVFP = 1
0x1E MVFP[5] Mirror image
0x1E MVFP[4] Vertical flip image
0x1E MVFP[2] Black Sun Enabled
0xAC STR-OPT = 0	Strobe Operation
0xAC STR-OPT[7] Strobe enable
0xAC STR-OPT[6] R/G/B controlled by STR_R,STR_G and STR_B
0xAC STR-OPT[5:4] Xenon Mode Option
00	1 row
01	2 rows
10	3 rows
11	4 rows
0xAC STR-OPT[1:0] Mode Selected
00	Xenon
01	LED 1
1x	LED 2

0x3A TSLB = 0x0D = 0000 1101	Line Buffer Test Options
bit[5] Negative Image

# Test Modes
Color Bar and other stuff.
Software is implement to use the color bar. There are two commands: colorbaryes, colorbarno. The various modes of the color bar are not implemented.
0x12 COM7 = 0
0x12 COM7[1] Enable/Disable color bar display.
0x42 COM17	= 0	Common Control 17
COM17[3] DSP Color Bar enable

0x70 SCALING_XSC = 0x3A = 0011 1010	Test Pattern Control and Horizontal Scaling
SCALING_XSC[7] Test Pattern Selection (see also SCALING_YSC[7])

0x71 SCALING_YSC = 0x35 = 0011 0101	Test Pattern Control and Vertical Scaling Register
SCALING_YSC[7] Test Pattern Selection (see also SCALING_XSC[7])

SCALING_XSC[7] & SCALING_YSC[7]
00 – no test output
01 – Shifting “1”
10 - 8-bar color bar
11 – Fade to gray color bar

# Timing
0x0F COM6 = 0x43 = 0100 0011 Common Control 6
0x11 CLKRC[7] Direct external clock = 1, bits[5:0] clock divider
0x6B DBLV	PLL and Regulator Control

0x15 COM10[6] HREF changes to HSYNC
0x15 COM10[5] PCLK Output Option Free run/Not Toggle during Horizontal blanking
0x15 COM10[4] PCLK reverse
0x15 COM10[3] HREF reverse
0x15 COM10[2] VSYNC changes on rising/falling edge of PCLK
0x15 COM10[1] VSYNC Negative
0x15 COM10[0] HSYNC Negative
0x17 HSTART Horizontal Frame start bits 8 of 11 see HREF
0x18 HSTOP Horizontal Frame stop bits 8 of 11 see HREF
0x19 VSTRT	Vertical start bits 8 of 10 see VREF
0x1A VSTOP	Vertical stop bits 8 of 10 see VREF
0x1B PSHFT Pixel Delay relative to HREF in pixels range 0 – 254
0x2A EXHCG[7:4] 4 MSB for dummy pixel insert in horizontal direction
0x2A EXHCG[3:2] HSYNC falling edge delay 2 MSB
0x2A EXHCG[1:0] HSYNC rising edge delay 2 MSB
0x2B EXHCL dummy Pixel Insert LSB – dummy pixel insert in horizontal direction
0x2D ADVFL LSB of Insert Dummy Lines in Vertical Direction (1 bit = 1 line)
0x2E ADVHV	MSB of insert Dummy Lines in Vertical Direction

0x30 HSYST	Horizontal Sync Rising Edge Delay (low 8 bits)

0x31 HSYEN	HSYNC Falling Edge Delay (low 8 bits)

0x32 HREF	HREF Control Register
bits[7:6] HREF edge offset to data output.
bits[5:3] HREF end 3 LSB (high 8 bits in HSTOP)
bits[2:0] HREF start 3 LSB (high 8 bits in HSTART)
0x92 DM_LNL	Dummy Line Count LSB
0x93 DM_LNH	Dummy Line Count MSB

# Windowing
Windowing has only been tested so far for the VGA format. It appears to work, but with some restrictions. The XSTART cannot be less than 13110 and the XSTOP can extend to over 70010. There are no apparent restrictions on the VSTRT and VSTOP values, within the range of 1 to 480? When the window values are read out for some of the “predefined” formats the XSTOP makes no sense. It is less than the XSTART value. Have no idea why this is true, but if you change it the output is not the lines and rows expected.
There is a routine for operating on the registers. The values are in 8 bit / 3 bit chunks for the H values and are in 8 bit / 2 bit chunks for the R values. This is handled by the window routine.
window[CR] – prints out the window as read from the registers.
window=[Hstart],[Hstop],[Vstart],[Vstop][CR] – sets the window registers the values are not checked	for validity.
0x03 VREF = 0
VREF[3:2] Lower 2 bits of VSTOP.
VREF[1:0] Lower 2 bits of VSTRT.
0x17 HSTART Horizontal Frame start bits 8 of 11 see HREF.
0x18 HSTOP Horizontal Frame stop bits 8 of 11 see HREF.
0x19 VSTRT	Vertical start bits 8 of 10 see VREF.
0x1A VSTOP	Vertical stop bits 8 of 10 see VREF.
0x32 HREF = 0x80 = 1000 0000
HREF[7:6] HREF edge offset to data output.
HREF[5:3] Three lower bits of HSTOP.
HREF[2:0] Three lower bits of HSTART.
# Camera Registers by Alpha Sequence
Format is Hex address, Register Name , default value.
BE,AD-CHB,0
C0,AD-CHGb,0
C1,AD-CHGr,0
BF,AD-CHR,0
2D,ADVFL,0
2E,ADVHV,0
25,AEB,63
24,AEW,75
6F,AWBCTR0,9A
6E,AWBCTR1,C0
6D,AWBCTR2,55
6C,AWBCTR3,2
27,BBIAS,80
A5,BD50MAX,F
9D,BD50ST,99
AB,BD60MAX,F
9E,BD60ST,7F
55,BRIGHT,0
11,CLKRC,80
15,COM10,2
3B,COM11,0
3C,COM12,68
3D,COM13,88
3E,COM14,0
40,COM15,C0
41,COM16,8
42,COM17,0
9,COM2,1
C,COM3,0
D,COM4,0
E,COM5,1
F,COM6,43
12,COM7,0
13,COM8,8F
14,COM9,4A
56,CONTRAS,40
57,CONTRAS_CENTER,80
6B,DBLV,A
93,DM_LNH,0
92,DM_LNL,0
4C,DNSTH,0
3F,EDGE,0
2B,EXHCL,0
2A,EXHCT,0
28,GbBIAS,80
69,GFIX,0
9F,HAECC1,C0
A0,HAECC2,90
A6,HAECC3,F0
A7,HAECC4,C1
A8,HAECC5,F0
A9,HAECC6,C1
AA,HAECC7,14
32,HREF,80
17,HSTART,11
18,HSTOP,61
31,HSYEN,30
30,HSYST,8
94,LCC6,50
95,LCC7,50
1C,MIDH,7F
1D,MIDL,A2
4F,MTX1,40
50,MTX2,34
51,MTX3,C
52,MTX4,17
53,MTX5,29
54,MTX6,40
58,MTXS,1E
1E,MVFP,1
A4,NT_CTRL,0
A,PID,76
1B,PSHFT,0
2C,RBIAS,80
4B,REG4B,0
74,REG74,0
75,REG75,F
76,REG76,1
77,REG77,10
8C,RGB444,0
C9,SATCTR,C0
72,SCALING_DCWCTR,11
A2,SCALING_PCLK_DELAY,R
70,SCALING_XSC,3A
71,SCALING_YSC,35
73,SCALING-PCLK_DIV,R
AC,STR-OPT,0
B5,THL_DLT,4
3A,TSLB,D
B,VER,73
26,VPT,D4
3,VREF,0
1A,VSTOP,7B
19,VSTRT,3

# Registers by Hex Address
Format as above Hex address, Register name and Default Value. NOTE: Registers marked as RESV are not shown. The sort is a mess the original spread sheet expects decimal or alpha.
3,VREF,0
9,COM2,1
11,CLKRC,80
12,COM7,0
13,COM8,8F
14,COM9,4A
15,COM10,2
17,HSTART,11
18,HSTOP,61
19,VSTRT,3
24,AEW,75
25,AEB,63
26,VPT,D4
27,BBIAS,80
28,GbBIAS,80
30,HSYST,8
31,HSYEN,30
32,HREF,80
40,COM15,C0
41,COM16,8
42,COM17,0
50,MTX2,34
51,MTX3,C
52,MTX4,17
53,MTX5,29
54,MTX6,40
55,BRIGHT,0
56,CONTRAS,40
57,CONTRAS_CENTER,80
58,MTXS,1E
69,GFIX,0
70,SCALING_XSC,3A
71,SCALING_YSC,35
72,SCALING_DCWCTR,11
73,SCALING-PCLK_DIV,R
74,REG74,0
75,REG75,F
76,REG76,1
77,REG77,10
92,DM_LNL,0
93,DM_LNH,0
94,LCC6,50
95,LCC7,50
1A,VSTOP,7B
1B,PSHFT,0
1C,MIDH,7F
1D,MIDL,A2
1E,MVFP,1
2A,EXHCT,0
2B,EXHCL,0
2C,RBIAS,80
2D,ADVFL,0
2E,ADVHV,0
3A,TSLB,D
3B,COM11,0
3C,COM12,68
3D,COM13,88
3E,COM14,0
3F,EDGE,0
4B,REG4B,0
4C,DNSTH,0
4F,MTX1,40
6B,DBLV,A
6C,AWBCTR3,2
6D,AWBCTR2,55
6E,AWBCTR1,C0
6F,AWBCTR0,9A
8C,RGB444,0
9D,BD50ST,99
9E,BD60ST,7F
9F,HAECC1,C0
A,PID,76
A0,HAECC2,90
A2,SCALING_PCLK_DELAY,R
A4,NT_CTRL,0
A5,BD50MAX,F
A6,HAECC3,F0
A7,HAECC4,C1
A8,HAECC5,F0
A9,HAECC6,C1
AA,HAECC7,14
AB,BD60MAX,F
AC,STR-OPT,0
B,VER,73
B5,THL_DLT,4
BE,AD-CHB,0
BF,AD-CHR,0
C,COM3,0
C0,AD-CHGb,0
C1,AD-CHGr,0
C9,SATCTR,C0
D,COM4,0
E,COM5,1
F,COM6,43